## Slide 1: Machine-Level Representation of Programs I

## Slide 2: Outline
Overview
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
Suggested reading
  Chap 3.1, 3.2, 3.3, 3.4, 3.5

## Slide 3: Characteristics of the high level programming languages
Abstraction
  Productive
  Reliable
Type checking
As efficient as hand written code
Can be compiled and executed on a number of different machines

## Slide 4: Characteristics of the assembly programming languages
Managing memory
Low level instructions to carry out the computation
Highly machine specific

## Slide 5: Why should we understand the assembly code
Understand the optimization capabilities of the compiler
Analyze the underlying inefficiencies in the code
Sometimes the run-time behavior of a program is needed

## Slide 6: From writing to understanding assembly code
Different set of skills
  Transformations
  Relation between source code and assembly code
Reverse engineering
  Trying to understand the process by which a system was created
    By studying the system and
    By working backward

## Slide 7: Understanding how compilation systems works
Optimizing Program Performance
Understanding link-time error
Avoid Security hole
  Buffer Overflow

## Slide 8: Outline
Overview
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move
Arithmetic & logical operations

## Slide 9: A Historical Perspective
Long evolutionary development
  Started from rather primitive 16-bit processors
  Added more features
    Take the advantage of the technology improvements
    Satisfy the demands for higher performance and for supporting more advanced operating systems
  Laden with features providing backward compatibility that are obsolete

## Slide 10: Intel x86 Processors
Dominate laptop/desktop/server market
Evolutionary design
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time goes on
Complex instruction set computer (CISC)
  Many different instructions with many different formats
    But, only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But, Intel has done just that!
    In terms of speed. Less so for low power.

## Slide 11: Intel x86 Evolution: Milestones
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit Intel processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32 bit Intel processor , referred to as IA32
  Added “flat addressing”, capable of running Unix
Pentium 4E 2004 125M 2800-3800
  First 64-bit Intel x86 processor, referred to as x86-64
Core 2 2006 291M 1060-3500
  First multi-core Intel processor
Core i7 2008 731M 1700-3900
  Four cores (our shark machines)

## Slide 12: Intel x86 Processors, cont.
Machine Evolution
  386 1985 0.3M
  Pentium 1993 3.1M
  Pentium/MMX 1997 4.5M
  PentiumPro 1995 6.5M
  Pentium III 1999 8.2M
  Pentium 4 2001 42M
  Core 2 Duo 2006 291M
  Core i7 2008 731M
Added Features
  Instructions to support multimedia operations
  Instructions to enable more efficient conditional operations
  Transition from 32 bits to 64 bits
  More cores

## Slide 13: 2015 State of the Art
  Core i7 Broadwell 2015
Desktop Model
  4 cores
  Integrated graphics
  3.3-3.8 GHz
  65W
Server Model
  8 cores
  Integrated I/O
  2-2.6 GHz
  45W

## Slide 14: x86 Clones: Advanced Micro Devices (AMD)
Historically
  AMD has followed just behind Intel
  A little bit slower, a lot cheaper
Then
  Recruited top circuit designers from Digital Equipment Corp. and other downward trending companies
  Built Opteron: tough competitor to Pentium 4
  Developed x86-64, their own extension to 64 bits
Recent Years
  Intel got its act together
    Leads the world in semiconductor technology
  AMD has fallen behind
    Relies on external semiconductor manufacturer

## Slide 15: Intel’s 64-Bit History
2001: Intel Attempts Radical Shift from IA32 to IA64
  Totally different architecture (Itanium)
  Executes IA32 code only as legacy
  Performance disappointing
2003: AMD Steps in with Evolutionary Solution
  x86-64 (now called “AMD64”)
Intel Felt Obligated to Focus on IA64
  Hard to admit mistake or that AMD is better
2004: Intel Announces EM64T extension to IA32
  Extended Memory 64-bit Technology
  Almost identical to x86-64!
All but low-end x86 processors support x86-64
  But, lots of code still runs in 32-bit mode

## Slide 16: Moor’s Law

## Slide 17: Outline
Overview
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move
Arithmetic & logical operations

## Slide 18: Levels of Abstraction
C programmer
Assembly programmer
Computer Designer
#include <stdio.h>
int main(){
int i, n = 10, t1 = 0, t2 = 1, nxt;
for (i = 1; i <= n; ++i){
printf("%d, ", t1);
nxt = t1 + t2;
t1 = t2;
t2 = nxt; }
return 0;
}
Gates, clocks, circuit layout, …
Seems like nice clean layers…

## Slide 19: Definitions
Architecture: (also ISA: instruction set architecture) The parts of a processor design that one needs to understand or write assembly/machine code.
  Examples: instruction set specification, registers.
Microarchitecture: Implementation of the architecture.
  Examples: cache sizes and core frequency.
Code Forms:
  Machine Code: The byte-level programs that a processor executes
  Assembly Code: A text representation of machine code
Example ISAs:
  Intel: x86, IA32, Itanium, x86-64
  ARM: Used in almost all mobile phones
  RISC-V: New open source ISA

## Slide 20: Assembly/Machine Code View
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte addressable array
    Code and user data
    Stack to support procedures

## Slide 21: Turning C into Object Code
text
text
binary
binary
Compiler (gcc –Og -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –Og p1.c p2.c -o p
    Use basic optimizations (-Og) [New to recent versions of GCC]
    Put resulting binary in file p

## Slide 22: Compiling Into Assembly
C Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Obtain (on shark machine) with command
  gcc –Og –S sum.c
Produces file sum.s
Warning: Will get very different results on different machines (Linux, Mac OS-X, …) due to different versions of gcc and different compiler settings.

## Slide 23: Assembly Characteristics: Data Types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
Code: Byte sequences encoding series of instructions
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 24: Assembly Characteristics: Operations
Perform arithmetic function on register or memory data
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches
  Indirect branches

## Slide 25: Object Code
Code for sumstore
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 14 bytes
  Each instruction 1, 3, or 5 bytes
  Starts at address 0x0400595

## Slide 26: Machine Instruction Example
C Code
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Object Code
  3-byte instruction
  Stored at address 0x40059e
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 27: Disassembling Object Code
Disassembled
Disassembler
  objdump –d sum
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
0000000000400595 <sumstore>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 28: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  gdb sum
  disassemble sumstore
  Disassemble procedure
  x/14xb sumstore
  Examine the 14 bytes starting at sumstore
Object
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3

## Slide 29: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91
Reverse engineering forbidden by
Microsoft End User License Agreement

## Slide 30: Outline
Overview
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move
Arithmetic & logical operations

## Slide 31: Operands
In high level languages
  Either constants
  Or variable
Example
  A = A + 4
variable
constant

## Slide 32: x86-64 Integer Registers
%rsp
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 33: Some History: IA32 Registers
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source
index
destination
index
stack
pointer
base
pointer
Origin
(mostly obsolete)

## Slide 34: Moving Data
Moving Data
  movq Source, Dest:
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “address modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN

## Slide 35: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest

## Slide 36: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 37: Virtual spaces
A linear array of bytes
  each with its own unique address (array index) starting at zero
… … … …
0xffffffff
0xfffffffe
0x2
0x1
0x0
addresses
contents

## Slide 38: Memory References
The name of the array is annotated as M
If addr is a memory address
M[addr] is the content of the memory starting at addr
addr is used as an array index
How many bytes are there in M[addr]?
  It depends on the context

## Slide 39: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 40: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 41: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 42: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 43: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 44: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 45: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 46: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 47: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 48: Addressing Mode
Type | Form | Operand value | Name
Immediate | $Imm | Imm | Immediate
Register | ra | R[ra] | Register
Memory | Imm | M[Imm] | Absolute
Memory | (ra) | M[R[ra]] | Indirect
Memory | Imm(rb) | M[Imm+ R[rb]] | Base+displacement
Memory | (rb, ri) | M[R[rb]+ R[ri]*s] | Indexed
Memory | Imm(rb, ri) | M[Imm+ R[rb]+ R[ri]] | Scaled indexed
Memory | (, ri, s) | M[R[ri]*s] | Scaled indexed
Memory | (rb, ri, s) | M[R[rb]+ R[ri]*s] | Scaled indexed
Memory | Imm(rb, ri, s) | M[Imm+ R[rb]+ R[ri]*s] | Scaled indexed

## Slide 49
Address | Value
0x100 | 0xFF
0x104 | 0xAB
0x108 | 0x13
0x10C | 0x11
Register | Value
%rax | 0x100
%rcx | 0x1
%rdx | 0x3
0x13
0x108
(0x108)0x13
260(%rcx,%rdx)
(0x10C)0x11
(%rax,%rdx,4)
0x108
$0x108
0xFF
(%rax)
0x100
%rax
Value
Operand

## Slide 50: Operations in Assembly Instructions
Performs only a very elementary operation
Normally one by one in sequential
Operate data stored in registers
Transfer data between memory and a register
Conditionally branch to a new instruction address

## Slide 51: Understanding Machine Execution
Where the sequence of instructions are stored?
  In virtual memory
  Code area
How the instructions are executed?
  %rip stores an address of memory, from the address,
  machine can read a whole instruction once
  then execute it
  increase %rip
    %rip is also called program counter (PC)

## Slide 52: Code Layout
kernel virtual memory
Read only code
Read only data
Read/write data
forbidden
memory invisible to
user code
Linux/x86
process
memory
image
0xffffffff
0xc0000000
0x08048000
%eip

## Slide 53: Addressing mode
Constant
& variable
f()
{
int i = 3 ;
}
Immediate & memory
00000000 <_f>:
0: 55 push %ebp
1: 89 e5 mov %esp,%ebp
3: 83 ec 14 sub $0x14,%esp
6: c7 45 fc movl ,
d: c9 leave
e: c3 ret
$0x3
03 00 00 00
-0x4(%ebp)

## Slide 54: Sequential execution
00000000 <_f>:
0: 55 push %ebp
1: 89 e5 mov %esp,%ebp
3: 83 ec 14 sub $0x14,%esp
6: c7 45 fc 03 00 00 00
movl $0x3,-0x4(%ebp)
d: c9 leave
e: c3 ret
 | c3 | ret
 | c9 | leave
c | 00 | 
 | 00 | 
 | 00 | 
 | 03 | 
8 | fc | 
 | 45 | 
 | c7 | movl $0x3,-0x4(%ebp)
 | 14 | 
4 | ec | 
 | 83 | sub $0x14,%esp
 | e5 | 
 | 89 | mov %esp,%ebp
0 | 55 | push %ebp
00 00 00 00
PC
00 00 00 01
PC
00 00 00 03
PC
00 00 00 06
PC
00 00 00 0d
PC
00 00 00 0e
PC

## Slide 55: Code Layout
kernel virtual memory
Read only code
Read only data
Read/write data
forbidden
memory invisible to
user code
Linux/x86
process
memory
image
0xffffffff
0xc0000000
0x08048000
%eip

## Slide 56: Data layout
Object model in assembly
  A large, byte-addressable array
  No distinctions even between signed or unsigned integers
  Code, user data, OS data
  Run-time stack for managing procedure call and return
  Blocks of memory allocated by user

## Slide 57: Data Types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
Code: Byte sequences encoding series of instructions

## Slide 58: Move Instructions
Format
  mov src, dest
  src and dest can only be one of the following
    Immediate
    Register
    Memory

## Slide 59: Move Instructions
Format
  The only possible combinations of the (src, dest) are
    (immediate, register)
    (memory, register) load
    (register, register)
    (immediate, memory) store
    (register, memory) store

## Slide 60: Data Movement
Instruction | Effect | Description
movl S, D | D  S | Move double word
movw S, D | D  S | Move word
movb S, D | D  S | Move byte
movsbl S, D | D  SignedExtend( S) | Move sign-extended byte
movzbl S, D | D  ZeroExtend(S) | Move zero-extended byte
pushq S | R[%rsp]  R[%rsp]-8 M[R[%rsp]]  S | Push
popq D | D  M[R[%rsp]] R[%rsp]  R[%rsp]+8 | Pop

## Slide 61: Data Movement Example
movl $0x4050, %eax immediate register
movw %bp, %sp register register
movb (%rdx, %rcx), %al memory register
movb $-17, (%rsp) immediate memory
movq %rax, -12(%rbp) register memory

## Slide 62: Data Formats
Move data instruction
  mov (general)
  movb (move byte)
  movw (move word)
  movl (move double word)
  movq (move quad word)

## Slide 63: Data Movement Example
Initial value %dh=8d %eax =98765432
movb %dh, %al %eax=9876548d
movsbl %dh, %eax %eax=ffffff8d
3 movzbl %dh, %eax %eax=0000008d

## Slide 64: Stack operation
Stack is a special kind of data structure
  It can store objects of the same type
The top of the stack must be explicitly specified
  It is denoted as top
There are two operations on the stack
  push and pop
There is a hardware stack in x86
  its bottom has high address number
  its top is indicated by %esp

## Slide 65: Stack Layout
kernel virtual memory
Read only code
Read only data
Read/write data
forbidden
memory invisible to
user code
Linux/x86 process
memory image
0xffffffff
0xc0000000
0x08048000
%eip
Stack
Downward growth
%esp

## Slide 66: Stack operation
There are two stack operation instructions
  Push and Pop
Push
  decreases the %rsp (enlarge the stack)
  stores the value in a register into the stack
Pop
  stores the value in the top of the stack into a register
  increases the %rsp (shrink the stack)

## Slide 67: Stack Operation
Instruction | Effect | Description
pushq S | R[%rsp]  R[%rsp]-8 M[R[%rsp]]  S | Push
popq D | D  M[R[%rsp]] R[%rsp]  R[%rsp]+8 | Pop

## Slide 68: Stack operations
%rax | 0x123
%rdx | 0
%rsp | 0x108
Increasing
address
pushq %rax ?
Stack “top”
0x108
%rsp

## Slide 69: Stack operations
%rax | 0x123
%rdx | 0
%rsp | 0x100
pushq %rax
popq %rdx ?
69
0x100
Stack “top”
0x123
0x108
%rsp

## Slide 70: Stack operations
%rax | 0x123
%rdx | 0x123
%rsp | 0x108
0x100
Stack “top”
0x123
0x108
%rsp
popq %rdx

## Slide 71: Outline
Overview
History of Intel processors and architectures
C, assembly, machine code
Assembly Basics: Registers, operands, move
Arithmetic & logical operations

## Slide 72: Address Computation Instruction
leaq Src, Dst
  Src is address mode expression
  Set Dst to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t <- x+x*2
salq $2, %rax # return t<<2
Converted to ASM by compiler:

## Slide 73: Examples for Lea Instruction
%rax holds x, %rcx holds y
6+x
leaq 6(%rax), %rdx
x+y
leaq (%rax, %rcx), %rdx
x+4*y
leaq (%rax, %rcx, 4), %rdx
7+9*x
leaq 7(%rax, %rax, 8), %rdx
9+x+2*y
leaq 9(%rax, %rcx, 2), %rdx
10+4*y
leaq 0xA(, %rcx, 4), %rdx
Result
Expression

## Slide 74: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src Also called shlq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order!
No distinction between signed and unsigned int (why?)

## Slide 75: Some Arithmetic Operations
One Operand Instructions
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
    notq Dest Dest = ~Dest
See book for more instructions
  Depending how you count, there are 2,034 total x86 instructions
  (If you count all addr modes, op widths, flags, it’s actually 3,683)

## Slide 76: Arithmetic Expression Example
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But, only used once
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret

## Slide 77: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | t1, t2, rval
%rdx | t4
%rcx | t5

## Slide 78: Arithmetic and Logical Operations
Address | Value
0x100 | 0xFF
0x104 | 0xAB
0x108 | 0x13
0x10C | 0x11
Register | Value
%eax | 0x100
%ecx | 0x1
%edx | 0x3
0xFD
%eax
subl %edx, %eax
0x0
%ecx
decl %ecx
0x14
0x108
incl 8(%eax)
0x110
0x10C
imull $16, (%eax, %edx, 4)
0xA8
0x104
subl %edx, 4(%eax)
0x100
0x100
addl %ecx, (%eax)
Value
Destination
Instruction

## Slide 79: Special Arithmetic Operations
imulq S | R[%rdx]:R[%rax] S*R[%rax] | Signed full multiply
mulq S | R[%rdx]:R[%rax] S*R[%rax] | Unsigned full multiply
clto | R[%rdx]:R[%rax]  SignExtend(R[%rax]) | Convert to oct word
idivq S | R[%rdx]  R[%rdx]:R[%rax] mod S R[%rax]  R[%rdx]:R[%rax]  S | Signed divide
divq S | R[%rdx] R[%rdx]:R[%rax] mod S R[%rax]  R[%rdx]:R[%rax]  S | Unsigned divide

## Slide 80: Machine Programming I: Summary
History of Intel processors and architectures
  Evolutionary design leads to many quirks and artifacts
C, assembly, machine code
  New forms of visible state: program counter, registers, ...
  Compiler must transform statements, expressions, procedures into low-level instruction sequences
Assembly Basics: Registers, operands, move
  The x86-64 move instructions cover wide range of data movement forms
Arithmetic
  C compiler will figure out different instruction combinations to carry out computation

## Slide 81: Backup Slides

## Slide 82: Data Movement Example
int main()
{
int a = 4 ;
/* “address of” operator creates a pointer */
int b = exchange(&a, 3);
printf(“a = %d, b = %d\n”, a, b);
}

## Slide 83: Data Movement Example
3
&a
%rsp
Offset
Stack
•
•
•
4
Can variable a be in a register?
a
b

## Slide 84: Data Movement Example
int exchange(int *xp, int y)
{
/* operator * performs deferencing */
int x = *xp ;
*xp = y ;
return x ;
}

## Slide 85: Data Movement Example
int exchange(int *xp, int y)
{
int x = *xp ;
*xp = y ;
return x ;
}
1 pushl %ebp
2 movl %esp, %ebp
3 movl 8(%ebp), %eax
4 movl 12(%ebp), %edx
5 movl (%eax), %ecx
6 movl %edx, (%eax)
7 movl %ecx, %eax
8 movl %ebp, %esp
9 popl %ebp

## Slide 86: Data Movement Example
3
&a
Rtn adr
%esp
Offset
Stack
•
•
•
4
a
b
y
xp

## Slide 87: Data Movement Example
3
&a
Rtn adr
Old %ebp
%esp
0
4
8
12
Offset
Stack
•
•
•
1 pushl %ebp
3
&a
Rtn adr
%esp
Offset
Stack
•
•
•
4
4
a
b
y
xp
a
b
y
xp

## Slide 88: Data Movement Example
3
&a
Rtn adr
Old %ebp
%ebp
%esp
0
4
8
12
Offset
Stack
•
•
•
2 movl %esp, %ebp
4
a
b
y
xp

## Slide 89: Data Movement Example
3 movl 8(%ebp), %eax
%eax: xp
How to represent xp by %ebp ?
20+%ebp
3
&a
Rtn adr
Old %ebp
%ebp
%esp
0
4
8
12
Offset
Stack
•
•
•
4
a
b
y
xp

## Slide 90: Data Movement Example
3 movl 8(%ebp), %eax
4 movl 12(%ebp), %edx
%eax: xp
%edx: 3
3
&a
Rtn adr
Old %ebp
%ebp
%esp
0
4
8
12
Offset
Stack
•
•
•
4
a
b
y
xp

## Slide 91: Data Movement Example
3 movl 8(%ebp), %eax
4 movl 12(%ebp), %edx
5 movl (%eax), %ecx
%eax: xp
%edx: 3
%ecx: 4
3
&a
Rtn adr
Old %ebp
%ebp
%esp
0
4
8
12
Offset
Stack
•
•
•
4
a
b
y
xp

## Slide 92: Data Movement Example
3 movl 8(%ebp), %eax
4 movl 12(%ebp), %edx
5 movl (%eax), %ecx
6 movl %edx, (%eax)
%eax: xp
%edx: 3
%ecx: 4
*xp(a): 3
3
&a
Rtn adr
Old %ebp
%ebp
%esp
0
4
8
12
Offset
Stack
•
•
•
3
a
b
y
xp

## Slide 93: Data Movement Example
3 movl 8(%ebp), %eax
4 movl 12(%ebp), %edx
5 movl (%eax), %ecx
6 movl %edx, (%eax)
7 movl %ecx, %eax
%eax: xp
%edx: y
%ecx: 4
*xp(a): 3
%eax: 4 (old *xp) return value
3
&a
Rtn adr
Old %ebp
%ebp
%esp
0
4
8
12
Offset
Stack
•
•
•
3
a
b
y
xp

## Slide 94: Data Movement Example
8 movl %ebp, %esp (do nothing)
9 popl %ebp
3
&a
Rtn adr
%esp
0
4
8
12
Offset
Stack
•
•
•
3
a
b
y
xp

## Slide 95: Data Movement Example
int main()
{
int a = 4 ;
/* “address of” operator creates a pointer */
int b = exchange(&a, 3);
printf(“a = %d, b = %d\n”, a, b);
}

## Slide 96: Data Movement Example
3
&a
%esp
Offset
Stack
•
•
•
3
%eax 4
Return value
b

## Slide 97: Data Movement Example
3
&a
%esp
Offset
Stack
•
•
•
4
3
b