## Slide 1: Machine-Level Representation of Programs III

## Slide 2: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 3: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Memory management
  Allocate during procedure execution
  Deallocate upon return
Mechanisms all implemented with machine instructions
x86-64 implementation of a procedure uses only those mechanisms required
P(…) {
•
•
y = Q(x);
print(y)
•
}
int Q(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}
Machine instructions implement the mechanisms, but the choices are determined by designers. These choices make up the Application Binary Interface (ABI).

## Slide 4: Outline
Procedures
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion
Suggested reading
  Chap 3.7

## Slide 5: x86-64 Stack
Carnegie Mellon
Region of memory managed with stack discipline
Memory viewed as array of bytes.
Different regions have different purposes.
(Like ABI, a policy decision)
code
stack
memory

## Slide 6: x86-64 Stack
Region of memory managed with stack discipline
Stack Pointer: %rsp
Stack “Top”
Stack “Bottom”
code
stack

## Slide 7: x86-64 Stack
Region of memory managed with stack discipline
Grows toward lower addresses
Register %rsp contains lowest stack address
  address of “top” element
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 8: x86-64 Stack: Push
pushq Src
  Fetch operand at Src
  Decrement %rsp by 8
  Write operand at address given by %rsp
-8
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %rsp
Stack “Top”

## Slide 9: x86-64 Stack: Pop
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (must be register)
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”
+8

## Slide 10: x86-64 Stack: Pop
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (usually a register)
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
val
(The memory doesn’t change, only the value of %rsp)
Stack “Bottom”
Stack “Top”

## Slide 11: Outline
Procedures
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 12: Code Examples
long mult2
(long a, long b)
{
long s = a * b;
return s;
}
void multstore
(long x, long y, long *dest) {
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
400557: retq # Return
0000000000400540 <multstore>:
400540: push %rbx # Save %rbx
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
400549: mov %rax,(%rbx) # Save at dest
40054c: pop %rbx # Restore %rbx
40054d: retq # Return

## Slide 13: Procedure Control Flow
Use stack to support procedure call and return
Procedure call: call label
  Push return address on stack
  Jump to label
Return address:
  Address of the next instruction right after call
  Example from disassembly
Procedure return: ret
  Pop address from stack
  Jump to address

## Slide 14: Control Flow Example #1
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400544
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 15: Control Flow Example #2
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400550
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip

## Slide 16: Control Flow Example #3
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400557
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip

## Slide 17: Control Flow Example #4
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400549
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 18: Outline
Procedures
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustrations of Recursion & Pointers

## Slide 19: Procedure Data Flow
Registers
First 6 arguments
Return value
Stack
Only allocate stack space when needed
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
Arg 7
• • •
Arg 8
Arg n
• • •

## Slide 20: Data Flow Examples
long mult2
(long a, long b)
{
long s = a * b;
return s;
}
void multstore
(long x, long y, long *dest) {
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
# a in %rdi, b in %rsi
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
# s in %rax
400557: retq # Return
0000000000400540 <multstore>:
# x in %rdi, y in %rsi, dest in %rdx
• • •
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
# t in %rax
400549: mov %rax,(%rbx) # Save at dest
• • •

## Slide 21: Outline
Procedures
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 22: Stack-Based Languages
Languages that support recursion
  e.g., C, Pascal, Java
  Code must be “Reentrant”
    Multiple simultaneous instantiations of single procedure
  Need some place to store state of each instantiation
    Arguments
    Local variables
    Return pointer
Stack discipline
  State for given procedure needed for limited time
    From when called to when return
  Callee returns before caller does
Stack allocated in Frames
  state for single procedure instantiation

## Slide 23: Call Chain Example
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
yoo
who
amI
amI
amI
Example
Call Chain
amI
Procedure amI() is recursive

## Slide 24: Stack Frames
Frame Pointer: %rbp
Contents
  Return information
  Local storage (if needed)
  Temporary space (if needed)
Management
  Space allocated when enter procedure
    “Set-up” code
    Includes push by call instruction
  Deallocated when return
    “Finish” code
    Includes pop by ret instruction
Stack Pointer: %rsp
Stack “Top”
Previous Frame
Frame for proc
(Optional) x

## Slide 25: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 26: Example
yoo(…)
{
•
•
who();
•
•
}
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 27: Example
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI(…)
{
•
•
amI();
•
•
}

## Slide 28: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 29: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 30: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 31: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 32: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 33: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 34: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 35: Example
yoo
who
amI
amI
amI
amI
yoo
%rbp
%rsp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 36: x86-64/Linux Stack Frame
Current Stack Frame (“Top” to Bottom)
  “Argument build:” Parameters for function about to call
  Local variables If can’t keep in registers
  Saved register context
  Old frame pointer (optional)
Caller Stack Frame
  Return address
    Pushed by call instruction
  Arguments for this call
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
(Optional)
Old %rbp
Arguments
7+
Caller
Frame
Frame pointer %rbp
Stack pointer
%rsp
(Optional)

## Slide 37: Local Variable
Callee Frame
Old %rbp
Local variable
Saved regs
Allocation
  Below saved regs or old %ebp
  movq/subq %rsp, (e.g., subq $4, %rsp)
De-allocation
  movq/addq %rsp, (e.g., addq $4, %rsp)
Usage
  Relative to %rsp/%rbp, (e.g., movq %rax, 8(%rsp))
%rbp
%rsp
retaddr

## Slide 38: Example: incr
long incr(long *p, long val) {
long x = *p;
long y = x + val;
*p = y;
return x;
}
incr:
movq (%rdi), %rax
addq %rax, %rsi
movq %rsi, (%rdi)
ret
Register | Use(s)
%rdi | Argument p
%rsi | Argument val, y
%rax | x, Return value

## Slide 39: Example: Calling incr #1
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8

## Slide 40: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 41: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000
Aside 1: movl $3000, %esi
Note: movl -> %exx zeros out high order 32 bits.
Why use movl instead of movq? 1 byte shorter.

## Slide 42: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000
Aside 2: leaq 8(%rsp), %rdi
Computes %rsp+8
Actually, used for what it is meant!

## Slide 43: Example: Calling incr #2
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 44: Example: Calling incr #3
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 45: Example: Calling incr #4
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rax | Return value
%rsp
Updated Stack Structure
. . .
Rtn address

## Slide 46: Example: Calling incr #5
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
Register | Use(s)
%rax | Return value
%rsp
Updated Stack Structure
. . .
Rtn address
%rsp
Final Stack Structure
. . .

## Slide 47: Register Saving Conventions
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can register be used for temporary storage?
  Contents of register %rdx overwritten by who
  This could be trouble ➙ something should be done!
    Need some coordination
yoo:
• • •
movq $15213, %rdx
call who
addq %rdx, %rax
• • •
ret
who:
• • •
subq $18213, %rdx
• • •
ret

## Slide 48: Register Saving Conventions
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can register be used for temporary storage?
Conventions
  “Caller Saved”
    Caller saves temporary values in its frame before the call
  “Callee Saved”
    Callee saves temporary values in its frame before using
    Callee restores them before returning to caller

## Slide 49: x86-64 Linux Register Usage #1
%rax
  Return value
  Also caller-saved
  Can be modified by procedure
%rdi, ..., %r9
  Arguments
  Also caller-saved
  Can be modified by procedure
%r10, %r11
  Caller-saved
  Can be modified by procedure
%rax
%rdx
%rcx
Return value
%r8
%r9
%r10
%r11
%rdi
%rsi
Arguments
Caller-saved
temporaries

## Slide 50: x86-64 Linux Register Usage #2
%rbx, %r12, %r13, %r14
  Callee-saved
  Callee must save & restore
%rbp
  Callee-saved
  Callee must save & restore
  May be used as frame pointer
  Can mix & match
%rsp
  Special form of callee save
  Restored to original value upon exit from procedure
%rbx
%rsp
Callee-saved
Temporaries
Special
%rbp
%r12
%r13
%r14

## Slide 51: Callee-Saved Example #1
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx

## Slide 52: Callee-Saved Example #2
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Pre-return Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx

## Slide 53: Put it Together
Caller Frame
%rbp
%rsp

## Slide 54: Put it Together
caller-save registers
1. Save caller-save registers (%rax, %rdi, ..., %r11)
Caller Frame
%rbp
%rsp

## Slide 55: Put it Together
arguments (n~1)
caller-save registers
1. Save caller-save registers (%rax, %rdi, ..., %r11)
2. Push actual arguments from right to left
Caller Frame
%rbp
%rsp

## Slide 56: Put it Together
arguments (n~1)
caller-save registers
1. Save caller-save registers (%rax, %rdi, ..., %r11)
2. Push actual arguments from right to left
3. Call instruction
  Save return address
  Transfer control to callee
retaddr
Caller Frame
%rbp
%rsp

## Slide 57: Put it Together
arguments (n~1)
4. Save caller %rbp
caller-save registers
old %rbp
retaddr
Caller Frame
%rbp
%rsp

## Slide 58: Put it Together
arguments (n~1)
4. Save caller %rbp
5. Set callee %rbp
caller-save registers
old %rbp
retaddr
Caller Frame
%rsp /
%rbp

## Slide 59: Put it Together
arguments (n~1)
4. Save caller %rbp
5. Set callee %rbp
6. Save callee-save registers (%rbx, %r12, %r13, %r14)
caller-save registers
old %rbp
retaddr
Caller Frame
callee-save registers
%rbp
%rsp

## Slide 60: Put it Together
arguments (n~1)
4. Save caller %rbp
5. Set callee %rbp
6. Save callee-save registers (%rbx, %r12, %r13, %r14)
7. Allocate space for local variable
caller-save registers
old %rbp
retaddr
Caller Frame
callee-save registers
local variables
%rbp
%rsp

## Slide 61: Put it Together
. . .
n-4. save return value in %rax
arguments (n~1)
caller-save registers
old %rbp
retaddr
Caller Frame
callee-save registers
local variables
%rbp
%rsp

## Slide 62: Put it Together
. . .
n-4. save return value in %rax
n-3. de-allocate local variable
arguments (n~1)
caller-save registers
old %rbp
retaddr
Caller Frame
callee-save registers
local variables
%rbp
%rsp

## Slide 63: Put it Together
. . .
n-4. save return value in %rax
n-3. de-allocate local variable
n-2. Restore callee-save registers
arguments (n~1)
caller-save registers
old %rbp
retaddr
Caller Frame
callee-save registers
local variables
%rbp
%rsp /

## Slide 64: Put it Together
. . .
n-4. save return value in %rax
n-3. de-allocate local variable
n-2. Restore callee-save registers
n-1. Restore caller %rbp
arguments (n~1)
caller-save registers
old %rbp
retaddr
Caller Frame
callee-save registers
local variables
%rbp
%rsp

## Slide 65: Put it Together
. . .
n-4. save return value in %rax
n-3. de-allocate local variable
n-2. Restore callee-save registers
n-1. Restore caller %rbp
n. Ret instruction
  pop return address
  Transfer control to caller
arguments (n~1)
caller-save registers
old %rbp
retaddr
Caller Frame
callee-save registers
local variables
%rbp
%rsp

## Slide 66: Outline
Procedures
  Stack Structure
  Calling Conventions
    Passing control
    Passing data
    Managing local data
  Illustration of Recursion

## Slide 67: Recursive Function
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi # (by 1)
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret

## Slide 68: Recursive Function Terminal Case
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi # (by 1)
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rax | Return value | Return value

## Slide 69: Recursive Function Register Save
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi # (by 1)
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rsp
. . .
Rtn address
Saved %rbx

## Slide 70: Recursive Function Call Setup
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi # (by 1)
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x >> 1 | Rec. argument
%rbx | x & 1 | Callee-saved

## Slide 71: Recursive Function Call
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi # (by 1)
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Recursive call return value | 

## Slide 72: Recursive Function Result
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi # (by 1)
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Return value | 

## Slide 73: Recursive Function Completion
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andl $1, %ebx
shrq %rdi # (by 1)
call pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rax | Return value | Return value
%rsp
. . .

## Slide 74: Observations About Recursion
Handled Without Special Consideration
  Stack frames mean that each function call has private storage
    Saved registers & local variables
    Saved return pointer
  Register saving conventions prevent one function call from corrupting another’s data
    Unless the C code explicitly does so (e.g., buffer overflow in Lecture 9)
  Stack discipline follows call / return pattern
    If P calls Q, then Q returns before P
    Last-In, First-Out
Also works for mutual recursion
  P calls Q; Q calls P

## Slide 75: x86-64 Procedure Summary
Important Points
  Stack is the right data structure for procedure call / return
    If P calls Q, then Q returns before P
Recursion (& mutual recursion) handled by normal calling conventions
  Can safely store values in local stack frame and in callee-saved registers
  Put function arguments at top of stack
  Result return in %rax
Pointers are addresses of values
  On stack or global
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %rbp
Arguments
7+
Caller
Frame
%rbp
(Optional)
%rsp